## Slide 1
CrowdSafe: CCTV-to-Alert Architecture
One-time calibration • Vision processing and zone features every 1 s • Forecasting, risk and alerts every 5 s
1. INPUT LAYER
Video stream + configuration
CCTV: fixed camera, 1080p, 25 fps
Administrator settings: zone polygons, exclusion masks
Risk bands: 2 / 4 / 5 persons/m²
Alert timing: hold 10 s, clear 30 s
2. CAMERA CALIBRATION | ONE-TIME SETUP
Shared geometry used by zone mapping and motion conversion
Inputs: measured desk/table dimensions, straight edges, camera height (if known)
Model: pinhole camera + radial distortion (k₁, k₂)
Outputs: camera parameters, zone masks Mz, visible floor area Az, pixel-to-floor mapping at 1.2 m head height
3. FRAME SAMPLING
Produces aligned frame(s) for both vision branches
One frame per second for counting
Partner frame at t + 0.2 s for RAFT
Resize / normalize; apply exclusion masks
4. PEOPLE COUNTING
Deployed zone path uses CLIP-EBC density map
CLIP-EBC ViT-B/16: zero-shot, NWPU weights
45 non-overlapping 224 px windows/frame
Output: density map Dt (135 × 240 cells)
YOLO11l / fusion: frame-level baselines only
5. MOTION FEATURE EXTRACTION
Input: paired frames + calibrated camera model
RAFT-large optical flow: 960 × 544 input, 12 iterations
Camera model → floor velocity (m/s), weighted by Dt
Per-zone: mean speed, speed variance, pressure (ρ·var), direction entropy, counter-flow
Inflow/outflow: trajectories only; unavailable from CCTV
6. ZONE AGGREGATION & UNIFIED FEATURE TABLE
Output: time-indexed zone feature rows at 1 Hz
Count: cz,t = Σ(Dt inside Mz) Density: ρz,t = cz,t / Az
Combine count, density and motion into one row per camera/run, zone and second
Trajectory sources (Jülich measured, JuPedSim simulated) populate the same feature schema
CCTV inflow/outflow fields remain unavailable
7. FORECASTING
Input: unified feature table • Output: forecast quantiles
Every 5 s: last 30 s of each zone's 1-Hz history
Chronos-2 zero-shot: per-zone or joint; quantiles p10 / p50 / p90
Baselines: persistence; physics fill-rate (trajectory data only)
Horizons: 10, 30, 60 s (120 s in simulation)
8. CONFORMAL CALIBRATION
Validation split calibrates; held-out test evaluates
Validation residual: r = ρtrue − p90
qh = 90 % conformal quantile of residuals
Calibrated upper bound: Uz,h = max(0, p90z,h + qh)
9. RISK CLASSIFICATION
Output: zone risk level + time-to-critical
Worst case: Wz = max(ρz, maxh Uz,h)
Low < 2 • Medium 2–4
High 4–5 • Critical ≥ 5 persons/m²
Time-to-critical: first horizon with Uz,h ≥ 5
10. ALERT GENERATION
Output: alert event
Raise when High/Critical persists for 10 s
Clear after below High for 30 s
Record zone, reason, forecast bound and time-to-critical
11. DASHBOARD & OUTPUTS
Operator view + logs / replay
Next.js dashboard: zone map, density, forecasts and alerts
FastAPI / WebSocket replay of stored runs
Stored: zone series, forecasts, risk states, alerts and stage latency
DATA FLOW: CCTV frames → CLIP-EBC density map + RAFT motion field → calibrated zone features → Chronos-2 quantiles → conformal upper bound → risk state → alert event → dashboard
Continuous operation: repeat frame sampling and vision extraction every second; refresh forecasting, risk classification and alert state every five seconds. YOLO11 / fusion are comparison baselines, not part of the deployed zone-density path.
pixel → floor
zone levels + forecasts (every zone)